## Slide 1: Preparation, Properties N Applications Of Kevlar And Its Structure

## Slide 2: Introduction to Kevlar

## Slide 3: What is Kevlar?
Kevlar is a high-strength synthetic fiber developed by DuPont.
It is a polyamide.
Chemical name is poly-para-phenylene terephthalamide (PPTA) It's known for its outstanding toughness, heat resistance, and lightweight properties.
Commonly used in bulletproof vests, tires, ropes, and more.
Liquid crystalline polymer
Condensation polymer
Thermosetting polymer

## Slide 4: Preparation of Kevlar

## Slide 5: Preparation Process: Polymerization Reaction
List the key raw materials:
p-Phenylenediamine (PPD)
Terephthaloyl chloride (TCl)
By-product formed is HCl
Solvents like N-methylpyrrolidone (NMP) or hexamethylphosphoramide (HMPA) and CaCl2

## Slide 6: Polymerization Process
Condensation reaction between PPD and TPC.
Formation of polymer chains through amide bonds.

## Slide 7: Step 1 – Synthesis of Polymer
Reaction:
PPD reacts with TPC in a solvent.
The reaction produces Kevlar chains and hydrochloric acid as a by-product.
Key Conditions:
Conducted in a controlled environment.
Reaction temperature: ~0°C to prevent side reactions.

## Slide 8: Step 2 – Spinning the Fibers
Dissolution:
The polymer is dissolved in concentrated sulfuric acid to produce a viscous spinning solution.
Fiber Formation:
Solution is extruded through spinnerets into an acid bath, forming solid fibers.

## Slide 9: Step 3 – Post-Treatment
Washing and Drying:
Fibers are thoroughly washed to remove residual acid and impurities.
Dried under controlled conditions to retain structural integrity.
Heat Treatment:
Enhances crystallinity and orientation of polymer chains, increasing tensile strength.

## Slide 10: Properties of Kevlar

## Slide 11: Mechanical Properties
High Tensile Strength:
Five times stronger than steel (per unit weight).
Lightweight:
Ideal for applications requiring strength without added bulk.
Flexibility:
Retains strength while being pliable.

## Slide 12: Thermal Properties
Heat Resistance:
  Decomposes at around 450°C without melting.
Low Thermal Conductivity:
  Effective in fire-resistant clothing.

## Slide 13: Chemical Properties
Chemical Resistance:
  Resists degradation by most chemicals, including acids and alkalis.
Low Reactivity:
  Stable under most environmental conditions.

## Slide 14: Electrical Properties
Non-Conductive:
  Used in electrical insulation.
High Dielectric Strength:
  Excellent for high-voltage environments.

## Slide 15: Advantages and Limitations
Advantages:
High strength-to-weight ratio
Heat and chemical resistance
Durability
Limitations:
Degradation under UV exposure
Expensive production

## Slide 16: Application of Kevlar

## Slide 17: Ballistic Protection
Bulletproof vests
Helmets
Armor for vehicles
Advantages:
  Lightweight and portable
  High-impact resistance

## Slide 18: Aerospace and Automotive
Aerospace: Reinforced parts in airplanes, spacecraft for weight reduction.
Automotive:
Brake pads
Tires
Reinforced car bodies
Benefits: Enhanced safety and fuel efficiency.

## Slide 19: Industrial Uses
Conveyor belts
Ropes and cables (marine and industrial)
Protective clothing for workers (gloves, aprons).
Advantages: Long lifespan, reduced maintenance.

## Slide 20: Sports and Recreation
Lightweight canoes and kayaks.
Racing sails.
Protective gear for athletes (helmets, gloves).

## Slide 21: Electronics and Telecommunications
Fiber-optic cables.
Reinforcement in smartphone components.

## Slide 22: Structure of Kevlar

## Slide 23: Chemical Structure of Kevlar
Molecular Formula: (C₁₄H₁₀N₂O₂)n
Chemical Name: Poly(paraphenylene terephthalamide)
Key Features:
Kevlar is a polymer with repeating units of aromatic polyamide (aramid).
It has strong amide bonds (-CO-NH-) between benzene rings.

## Slide 24: Molecular Structure of Kevlar
Structure Visualization:
Linear chains of aromatic rings linked by amide groups.
The chains are highly oriented, leading to strong intermolecular hydrogen bonding.
Diagram: (Include an illustration of the molecular structure, with labeled amide groups and hydrogen bonds)

## Slide 25: Hydrogen Bonding and Its Impact
Hydrogen Bonding:
Kevlar's strength is due to hydrogen bonds between adjacent polymer chains.
These bonds contribute to its high tensile strength and thermal stability.
Key Impact:
High tensile strength (up to 3,620 MPa).
Resistant to abrasion and high temperatures.

## Slide 26: Microstructure of Kevlar Fibers
Fiber Alignment:
Kevlar fibers are highly crystalline.
The polymer chains align parallel to the fiber axis, increasing strength.
Properties:
High modulus of elasticity (83 GPa).
Lightweight and flexible.

## Slide 27: Comparison with Other Materials
Comparison Table: Kevlar vs. Steel vs. Nylon
  Strength-to-weight ratio: Kevlar is 5 times stronger than steel.
  Density: Kevlar is lighter than both steel and nylon.
  Thermal Resistance: Kevlar withstands temperatures up to 450°C without melting.

## Slide 28: Conclusion
Summary:
Kevlar’s unique structure offers exceptional strength and durability.
Widely used in various industries for protective and high-performance applications.
Future Outlook:
Potential innovations in lighter and more cost-effective aramid fibers.

## Slide 29: Thank you
Credits:
Alen Roy Thomas
Agatha S Rajesh
Amana Shema S J